## Slide 1: PGY630: Quantitative methods for biomedical research Image processing basics: file formats, bit depth, and compression Kenneth S. Campbell, PhD

## Slide 2: Objectives
    Explain how computers store image data, including details about the number of pixels, bit resolution and color-spaces
    Recognize that different image formats have distinct strengths and weaknesses
    Recall the difference between bitmap and vector-based formats and know when to use each

## Slide 3: Raw data normally come as bitmaps
Cameras and scanners use many small sensors
  Each sensor gives 1 pixel
  For example, at one point in time, the iPhone camera had 8 megapixels (3264 x 2418)

## Slide 4: Bitmaps

## Slide 5: Bitmaps
0 | 0 | 1
1 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1

## Slide 6: Color schemes
Many possible schemes (L*a*b, HSV, HSL, CMYK)
Most common in our type of science is RGB
  3 numbers to describe the amount of Red, Green and Blue
  The maximum value of each number depends on the bit-depth
  8-bit is, or at least used to be, the most common

## Slide 7: What is bit-depth?
The number of binary digits for each color
  8 bit means numbers can range from 0000 0000 to 1111 1111 (that is, 0 to 28 = 255)
  16 bit means numbers can range from 0000 0000 0000 0000 to 1111 1111 1111 1111 (that is, 0 to 216 = 65,536)
  More bits means more potential colors but requires more memory

## Slide 8: An example of an 8 bit RGB image
0
255
0
0
255
0
255
127
255
0
0
255
127
255
0
255
127
0
0
255
0
127
255
255
0
127
0
Red
Green
Blue

## Slide 9: Examples of different bit-depths
Wikipedia
24 bit
4 bit
8 bit
2 bit
1 bit

## Slide 10: Common sense rules about bit levels
You only have the information you collected in the original picture
Converting to higher bit level (e.g. 8 bit to 12 bit) uses more memory and takes more time but doesn’t give you anything extra
Converting to a lower bit level (e.g. 12 bit to 8 bit) throws away information

## Slide 11: Compresion
Storing the picture in less memory than a straight pixel by pixel description
Lossless compression
  Stores the same information (*.png)
Lossy compression
  Stores a variant, thus can’t go back to the original
  Generally takes less memory, and is thus quicker to send between computers (*.jpg)

## Slide 12: Compression
0 | 0 | 0
0 | 0 | 0
0 | 1 | 0
0 | 0 | 0
0 | 0 | 0

## Slide 13: Compression
0 | 0 | 0
0 | 0 | 0
0 | 1 | 0
0 | 0 | 0
0 | 0 | 0
or
Every pixel is black, except (3,2)

## Slide 14: Image formats
Vector-based | Bitmap | 
 | Lossless | Lossy
Describes a picture using ‘geometrical primitives’ (lines, curves, polygons) | Describes a picture using pixels | 
Scalable (Can change size without problems) | Not scalable (Cannot change size without problems) | 
Interchangeable (can go from one to another and back) | Interchangeable | Not interchangeable (going from one to another and back, gives something new)

## Slide 15: Vector versus bitmap
From Wikipedia

## Slide 16: Image formats
Vector-based | Bitmap | 
 | Lossless | Lossy
.eps (Illustrator) | .tif (sometimes) | .jpg
.ai (Illustrator) | .png | .gif
.svg (InkScape | .bmp | 
.wmf (Win clipboard) | .psd (Photoshop) | 
.emf |  | 
.pdf |  | 
.pict (old Mac clipboard) |  | 

## Slide 17: Common sense rules
Try to understand what you are doing
  Don’t just copy what the person before did
If you only want 1 simple rule (but you probably shouldn’t after taking this class), it’s hard to beat the *.png format
Test your analysis to see if you get the same result with re-sized images
  Smaller images will save computation time

## Slide 18: Common sense rules 2
Use vector-based formats whenever possible
  Illustrator, Inkscape are great for making figures
  Export from SigmaPlot, Prism etc, into vector formats
If you have to use bitmaps, use lossless formats
  Warning, formats have multiple options (For example, you can store jpgs inside tifs)
  Use highest quality settings
  Check quality – compare final versions to originals

## Slide 19: Objectives
    Explain how computers store image data, including details about the number of pixels, bit resolution and color-spaces
    Recognize that different image formats have distinct strengths and weaknesses
    Recall the difference between bitmap and vector-based formats and know when to use each
    Write MATLAB code to create or open image files, resize images, and display them